## Slide 1
This guidance is developed by:
GAZA Shelter Response - September 2025
Liability Disclaimer
This guidance is intended for basic, household-level visual checks only. It does not constitute structural or safety certification and cannot guarantee a building is safe to enter or occupy. Conditions may change suddenly and without warning.
A full damage assessment by qualified professionals is required to verify structural stability.
If any sign of serious danger is present, do not enter and seek qualified professional assistance if available.
Ask for permission from the owner
Assess the damage, as best you can
Written permission, or a verbal agreement.
Carefully assess the safety of your home.
A. Before using any house or property
B. Outside Check
Parts of the
building collapsed
or leaning ​
Deep cracks
in exterior
walls
Leaning
or bulging walls
Walk around the building (if possible) and look for major structural issues.
DO NOT ENTER IF YOU SEE:
Loose & large pieces at risk of falling.
Guidance for the Temporary Occupancy of Damaged Buildings
Note: This tool offers basic guidance only and is not a substitute for expert structural assessment. (Partners to insert hotline or contact information)
even if they are still standing.
Due to: Collapsing debris, hazardous materials, structural damage
Burnt buildings are
…DANGEROUS…
Notes: Body Text
10 pt to 11 pt – Ideal for standard reading comfort.
Use 11 pt if your audience might prefer slightly larger text (e.g., older readers).
Use 10 pt for more compact layouts or technical content.
🧠 Headings
Main Title: 18–24 pt
Section Headings: 14–16 pt
Subheadings: 12–14 pt
📌 Captions / Footnotes
8–9 pt – Small but still readable.

## Slide 2
Always enter with someone else
!! BUT NOT CHILDREN !!
BE CAREFUL of any exposed electrical
cables or damaged appliances.
C. Inside Check
If the exterior seems sound:
Enter the building during daylight.
Wear sensible clothing, or proper protective clothing if available.
Cover your mouth and nose before
entering.
Check stability with your foot
before fully standing in a specific area.
Initial Visual Inspection
2. Inspect walls in each room
Wall to ceiling cracks
Diagonal Cracks
Are any beams or slabs cracked or bending?
Are there STRUCTURAL cracks??
especially at corners of doors or windows
Consider the whole building,
not just the rooms you want to occupy.
Floor and ceiling cracks
Stairstep crack in brick or masonry
Bowed wall
2
1. Check ceiling & beam
Carefully inspect the ceiling, columns, beams, and walls. Do not occupy the space unless you are certain it is structurally safe.
Do not touch unidentified objects, they may be unexploded ordnance, and ensure your family, including children, are warned not to approach or handle them.
Contact Civil Defence to inform of the unexploded ordnance.
Note: This tool offers basic guidance only and is not a substitute for expert structural assessment. (Partners to insert hotline or contact information)
Note: This tool offers basic guidance only and is not a substitute for expert structural assessment. (Partners to insert hotline or contact information)
Cracked or shifted column

## Slide 3
4
Badly fitting doors (e.g. a door that jams or doesn’t fit its frame) can be a sign the building has shifted.
3. Check floors & roof
Do the floors feel soft? Or sagging?
They could collapse or crumble further if stepped on.
Proceed only if you are confident that it is safe.
Floor and wall gaps
Sagging floors
4. Check stairs
Loose or broken steps.
Cracks in the stair structure or supports.
Signs of shifting or tilting.
Clear debris carefully, as they may pose a tripping hazard.
Avoid stairs lead to upper floors of the building with visible damage
5. Check doors & windows
Cracked or shattered glass or wood.
Loose or hanging frames.
Difficulty opening or closing.
Sharp edges or debris around openings.
Signs of structural damage around the window area
Note: This tool offers basic guidance only and is not a substitute for expert structural assessment. (Partners to insert hotline or contact information)
Note: This tool offers basic guidance only and is not a substitute for expert structural assessment. (Partners to insert hotline or contact information)

## Slide 4
6
Expanded Sealing Off Materials
Essential Components
TIMBER BATTEN
5x2.5cm, useful for creating dividing partitions, fixing tarpaulin and sheet to walls. 2.4m lengths.
20 pcs
TARPAULINS
woven plastic, available in sizes of 6x4 meters, 5x4 meters, or as a roll of 4 meters width. They can be used for roofing, walls and covering openings/windows
3 pcs
Clout nails 40mm
For timber connections. Used for making frames and fixing cover-battens.
0.25 kg
NAILS 50mm
For timber connections. Used for making frames and fixing cover-battens.
0.5 kg
NAILS 75 mm
For timber connections. Used for making frames and fixing cover-battens.
0.5 kg
ROPE
Minimum 30 meters length, in roll, 6mm thickness.
1 roll
HAND SAW
total length 60 cm, for wood, good quality, tempered, hardened and set teeth. Unbreakable handle.
MEASURING TAPE
3 meters, graduated in centimetres.
2 pcs
1 pcs
Optional Components
TIMBER SHEET - PLYWOOD OR OSB
Approx. 1 cm thick, used for internal partitions, covering openings etc. 2.4x1.2 m.
32 pcs
METAL FIXING BAND
10m roll, 20mm width x 0.9 thick. Useful for general purpose fixing band.
1 pcs
These materials are recommended for emergency repairs. Partners are encouraged to modify the quantities below based on the materials and resources available to them.
HAMMER
Metal or fiberglass handle.
1 pcs
PLASTIC SHEET
0.3mm thick, roll is up to 50sqm per shelter. Minimum width 4m.
1 roll
SCALPEL
Precision cutting tool with replaceable blade. Used for fixing tarpaulins.
1 pcs
Note: This tool offers basic guidance only and is not a substitute for expert structural assessment. (Partners to insert hotline or contact information)
Note: This tool offers basic guidance only and is not a substitute for expert structural assessment. (Partners to insert hotline or contact information)

## Slide 5
8
Wear gloves &
carefully remove shattered glass
Secure tarpaulin
Use timber & nails or ropes to tightly cover the opening.
Add barrier
Install a railing to prevent accidents
1m
Reuse old doors
Adjust them to fit the size of the openings
Keep children away from insecure windows
Sealing off openings
Sealing off large gaps or collapsed areas
Sealing-off internal walls
Rebuild with:
If blocks are unavailable, use:
  Wooden boards
  CGI sheets
  Tightly secure fabric/tarpaulin
Use fabric, tarps, old doors, or wood to create privacy in damaged spaces.
Salvaged blocks ​
Cement & sand
Mud & straw
Note: This tool offers basic guidance only and is not a substitute for expert structural assessment. (Partners to insert hotline or contact information)
Note: This tool offers basic guidance only and is not a substitute for expert structural assessment. (Partners to insert hotline or contact information)

## Slide 6
10
Sealing off roofs
If it is difficult to get a good fixing to blockwork, try using a wooden wedge.
1. Hammer the wedge into a joint in the blocks
2. Cut it off flush
3. Nail the batten to the wedge
When fixing a timber batten to blockwork wall:
Try using metal straps to get a good fixing
Try nailing into the mortar joints
When fixing a tarpaulin to blockwork wall:
Use a timber batten
Wrap around a timber batten
How to fix timber to blockwork?
Cover holes with metal sheets or tarpaulin.
For large gaps, use wooden beams and secure tarps with rope or wire.
Tarps provide shade,
rain protection, and privacy.
This method can be also applied with clout nails or scalpel
Note: This tool offers basic guidance only and is not a substitute for expert structural assessment. (Partners to insert hotline or contact information)
Note: This tool offers basic guidance only and is not a substitute for expert structural assessment. (Partners to insert hotline or contact information)

## Slide 7
12
Safe handling of Asbestos
Recognising Asbestos
Health Risks
In Gaza, the most common asbestos is found in roofing sheets, mainly in refugee camps.
Corrugated cement-like panels with a wavy, corrugated profile
Cloudy grey, sometimes with rough, grainy, or speckled patches caused by aging cement and exposed fibers.
When asbestos-containing materials are disturbed, tiny fibres are released into the air.
If inhaled  Serious health issues such as cancer.
Protect your mouth and nose with a mask using a t-shirt or fabric across your mouth and nose.
Put it in a plastic bag –and then put that plastic bag inside another plastic bag (double bagging). Seal with some tape if you have it. ​
Do not break it up into pieces. Avoid creating dust .
When finished dispose the mask in the 2nd bag.
How to remove asbestos panels?
Disposal of Asbestos
Put the asbestos bags to one side.
Note: This tool offers basic guidance only and is not a substitute for expert structural assessment. (Partners to insert hotline or contact information)
Note: This tool offers basic guidance only and is not a substitute for expert structural assessment. (Partners to insert hotline or contact information)
Content adapted from
Asbestos should preferably be handled by experts due to associated health risks.

## Slide 8
14
COOKING AND LIGHTING – FIRE PREVENTION AND HEALTH RISKS
Keep the flame enclosed in a stove or metal cage
Raise the stove using bricks
It’s best to cook in outdoor areas, away from any flammable materials, to reduce the risk of fire.
If it's not possible and you have to cook inside the same area you're occupying, make sure to:
Don't let the stove unattended
Use a metal/ clay barrier around the stove if available
Keep distance between the walls and the stove
Ensure ventilation while cooking
Keep the fire away from any flammable materials and children.
If candles are used, try to secure them in a non-combustible holders.
Be aware of fire and health risks such as oil or kerosene lamps and candles.
Keep in mind:
Note: This tool offers basic guidance only and is not a substitute for expert structural assessment. (Partners to insert hotline or contact information)
Note: This tool offers basic guidance only and is not a substitute for expert structural assessment. (Partners to insert hotline or contact information)
Avoid an open flame
Ensure the stove is turned off completely after use.