## Slide 1
Optional Components
Timber sheet (Plywood or OSB), Approx. 1 cm thick, used for creating beams, trusses, doors, bracing, raised floors, and internal cladding. | Pcs | 3 | 
Plastic sheet, 0.3mm thick, roll is up to 50 sqm per shelter. Minimum width 4 m. | Sqm | 50 | 
Emergency Shelter Kit
This IEC indicates techniques to assemble a shelter and does not prescribe a specific shelter design. Partners are encouraged to modify the quantities below based on the materials, resources, and space available to them.
For a video demonstration, refer to the ESK: Shelter Kit Construction Video | Shelter Cluster
Essential Components
Component | Unit | Quantity | Indicative Picture
Timber, untreated, essential for frame construction, required to be at least 2.4 meters in length. This IEC is for cross-sections of 5cm x 2.5cm | Pcs | 114 | 
Tarpaulins, woven plastic, available in sizes of 6x4 meters, 5x4 meters, or as a roll of 4 meters width. They can be used for roofing, walls and flooring. | Pcs | 3 | 
Nails, 5 cm nails for timber connections. Used for structural joints and fixing cover-battens. | Kg | 1.6 | 
Rope, Minimum 30 meters length, in roll, 6mm thickness. | Lm | 30 | 
Hand saw, total length 60 cm, for wood, good quality, tempered, hardened and set teeth. Unbreakable handle. | Pcs | 2-3 | 
Measuring tape, 3 meters, graduated in centimeters. | Pcs | 1 | 
Hammer, metal or fiberglass handle. | Pcs | 1 | 
This IEC has been developed by

## Slide 2: How to Build Wall Panels
a=2.4 m
a= 2.4 m
Thin edge = 2.5cm
5cm nails
2.5cm
5cm
2.5cm
30 cm
5cm nails
The tarpaulin holds the frame square and so should be pulled tight, but not so tight that it bends the timber.
Tarpaulin fixed
= Panel held square
= Remove temporary bracing
The frame is constructed as a T-section which makes it strong
Pull tarpaulin tight
Flip it
1. Lay out the pieces of timber, standing them up on the thin edge.
2. Nail the timber together using 5cm nails.
To check if the panel is square: measure the two diagonal measurements, should be equal.
3. Add temporary bracing, of any size, to hold it square then flip it to fix the tarpaulin on the frame.
4. Lay the tarpaulin over the frame. Leaving a 60cm outside the bottom edge of the frame, to avoid filtration and to favor the anchorage.
5. Fix on the 5 x 2.5cm cover battens with
5 cm nails every 30cm.
Fix Tarpaulin
60 cm
Temporary bracing
a
a
//
//
//
//
a
This IEC has been developed by

## Slide 3
Is the shelter square? Measure the diagonals, should be the same.
The panels are connected together while still flat on the ground. The cover-batten is used to make a strong connection. Once the wall panel has been lifted into position, then the two vertical studs must also be nailed together.
Lift the panels together
How the corner is joined together?
Connect the corners securely using:
Add corner bracing
Skirting = 60cm
Skirting = 60cm
Plan view
5cm nails
30 cm
How to Connect Wall Panels
Panel 2
Panel 1
B. Connect the panels together by nailing the cover-batten
5cm nails
5cm nail
Panel 1
A. Move Panel 2 closer to Panel 1
Panel 1 cover-batten
Tarpaulin
Panel 2
Panel 1 cover-
batten
This IEC has been developed by
C. Nail the vertical studs timbers once the panels are lifted

## Slide 4: Roofing: Pitched Roof
The horizontal pieces of timber are doubled, one on either side.
1.928 m
2.4m
7.87 m
15°
3.7m
If OSB or plywood is available, then this truss with ‘gusset plates’ is a good option with strong connections.
1.928 m
2.4m
15°
If short of timber, this is a good option. Strong connections are made with pieces of used tin cans.
1.928 m
2.4 m
15°
3.7m
3.7m
To ensure uniformity and save time, construct all trusses simultaneously by stacking them one on top of the other or using one as a template.
This approach guarantees that each truss is identical and reduces the risk of errors during the assembly process.
HELPFUL
TIP
This IEC has been developed by

## Slide 5: How to Build Roof Trusses
This IEC has been developed by
Diagonal braces need to be fixed, one at either end. These are fixed to the underside of the first and second truss and the final two trusses.
The trusses are placed one by one and fixed to the wall plate
Tarp
Cover batten
Truss
Wall panel
The long horizontal piece at the ridge of the roof should be 2 x 2.4m lengths. They join the trusses together and also provide a support for the tarpaulin.
5cm nails
Wall plate
2.4m
2.4m
Diagonal bracing
The short off-cuts and cover battens are there to secure the top of the tarpaulin.

## Slide 6
This IEC has been developed by
How to Cover the Roof
Fold the Tarpaulin to facilitate its raising to the roof
2. Progressively unroll the tarpaulin over the roof structure - start from middle
3. Add timber cover battens and short off-cuts to pin roof tarp
The cover battens are there to secure the top of the tarpaulin.
Cover batten
Tarp
Cover batten
Truss
Wall panel
First fold: Fold the left-hand edge towards the centre line
Second fold: Fold again to the centre.
Repeat for the right-hand edge
Finally: Fold to the centre as shown.
5cm nails
30 cm
Truss - Tarp - Timber wall connection

## Slide 7: How to Fix Shelter on Ground
This IEC has been developed by
D- FIRM GROUND:
The type of anchoring, or foundation, will depend on the ground conditions.
Weighing down the tarpaulin “skirt” is the simplest method and suitable for soft or sandy ground, and a concrete slab. Buried sandbags at each corner, or close to each corner, is another option for sandy ground
Driving, or burying, wooden stakes into the ground is only
suitable for firm ground.
OUTSIDE
INSIDE
Tarpaulin
Cover-batten
OUTSIDE
INSIDE
Tarpaulin
Cover-batten
Cross-brace
Rocks, rubble sandbag
Tarpaulin
Coverbatten
OUTSIDE
INSIDE
Concrete slab
With rubble and old rebar available, this is an appropriate
anchoring or foundation detail.
Steel bar (10mm max)
Hooked at the bottom, bent
over the panel at the top
Fill the hole with rubble, using larger pieces at the bottom.
Fill the voids with sand, dirt or soil.
Steel mesh/bars
Rocks and rubble
Tarpaulin in ground
B- SOFT/SANDY GROUND:
A- SOFT/SANDY GROUND AND HARD SURFACE:
Steel bar
C- SOFT/SANDY GROUND:
Anchoring with sandbags can be replaced with:
Brick/ hollow blocks/ or concrete
In exposed areas, the use of guy-ropes is recommended
60cm
OUTSIDE
INSIDE
Tarpaulin
Coverbatten
Rope
Rocks, rubble sandbag

## Slide 8: How to Cover the Shelter Floor
Floor Covering (Cardboard / Carpet, …)
Plastic Sheet (Optional)
Plastic Sheet as Damp Proof Membrane (DPM)
Sand fill
Floor Covering (Cardboard / Carpet, …)
Brick / Block Paving
Plastic Sheet as Damp Proof Membrane (DPM)
It is a good idea to have a raised floor inside the shelter that is kept dry and contained by a plastic sheet (a damp-proof membrane - DPM).
This can be achieved in a number of ways:
1. Simply covering the inside with plastic sheet, carpet or even cardboard.
2. Raising the ground level with rubble, bricks, broken blocks; filling the gaps with sand; and covering with a suitable flooring. A plastic sheet DPM is advised if available.
3. A good solution would be to use wooden pallets to construct a level raised floor.
Floor deck(Timber, OSB)
Timber
Plastic Sheet as Damp Proof Membrane (DPM)
OUTSIDE
OUTSIDE
OUTSIDE
This IEC has been developed by